## Slide 1: Traffic Calming Toolbox
Craig Toocheck and Paige Anderson
Staff Engineers
Department of Mobility & Infrastructure
City of Pittsburgh
Lawrenceville United
July 16, 2019

## Slide 2: SAFER STREETS
Slow speeds
Lower volumes
Improved crossings

## Slide 3: Calming Traffic
Visual controls
Vertical controls
Horizontal controls
Operational controls

## Slide 4: 1. VISUAL CONTROLS: MAKE STREETS (SEEM) SMALLER
Slows speeds

## Slide 5: On Street Parking
Characteristics
  Visually narrows the street
  Creates friction and uncertainty which slows speeds
Typical use
  Most street types
Considerations
  Not effective where parking demand is low
  Must have adequate space to ensure safety
Visual Control

## Slide 6: Yield Streets
Characteristics
  Narrow bi-directional travel ways force drivers to slow and yield when approaching opposing traffic.
Typical use
  Appropriate to low volume residential streets or most alleys.
Considerations
  Emergency vehicle access and movement.
  Vehicle volumes.
  Street width and availability of open curbside space to pull over.
Visual Control

## Slide 7: Narrow Lanes
Characteristics
  Visually or physically narrow travel ways
Typical use
  Visual narrowing is appropriate on most street types
  Actual narrow travel ways appropriate to low volume streets
Considerations
  Maintenance of striping
  Movement of vehicles on yield streets
Visual Control

## Slide 8: Vertical enclosure
Characteristics
  Vertical edge to the street
  Gives a sense of enclosure naturally slowing travel speeds
Typical use
  Any street type
Considerations
  Can be accomplished with built structures or street trees
  The closer together vertical elements are, the more effective the traffic calming effect
  Trees take time to grow; large buildings are not appropriate in all contexts
Visual Control

## Slide 9: 2. Vertical CONTROLS: elements to force slower speeds or negotiation
Slows speeds

## Slide 10: Speed Hump
Characteristics
  Gentle grade
  Moderately slow design speed (15 – 20 MPH)
Typical use
  Low and moderate volume residential and mixed use streets
Considerations
  Snow removal and maintenance
  Not appropriate on hills with grades over 8%
Vertical Control
Gentler than speed “bumps”

## Slide 11: Raised Crosswalk
Characteristics
  Slows speeds at crossings
  Moderately slow design speed (15 – 20 MPH)
Typical use
  Low to moderate volume streets
  Marked crosswalks
  Midblock locations
Considerations
  Crossing must be at safe location
  Pedestrian demand volumes
  Drainage
Vertical Control

## Slide 12: Raised Intersection
Characteristics
  Crosswalks and intersection interior are raised above street grade
  Often includes mixed patterns or materials
Typical use
  Commercial street intersections
  High pedestrian volume areas
Considerations
  Cost
  Pedestrian volumes
  Maintenance
  Drainage
Vertical Control

## Slide 13
3. HORIZONTAL CONTROLS:
Narrow street or force shifting to slow speeds

## Slide 14: Raised Median
Characteristics
  Paved or vegetated area raised above street grade separating traffic lanes
Typical use
  Moderate to higher volume streets
  Typically better on streets with few vehicle access points
Considerations
  Cost
  Maintenance
  Driveways
  Grade and sightlines
  Pedestrian crossings
Horizontal Control

## Slide 15: CURB EXTENSION / BUMPOUT
Characteristics
  Extension of the curbline toward the centerline of the street
  Can be achieved via physical curb, paint, pavement removal or other techniques
  Improves visibility of people crossing
Typical use
  Appropriate on most street types
  Paired with crosswalks can narrow pedestrian crossing distance and improve visibility
Considerations
  Street cleaning and snow removal
  Maintenance and cost
  Drainage
Horizontal Control

## Slide 16: Choker / Neckdown
Characteristics
  Pair of bulbouts narrowing the travelway of the street
Typical use
  Low to moderate volume streets
Considerations
  Street cleaning and snow removal
  Maintenance and cost
  Drainage
Horizontal Control

## Slide 17: TIGHTER Corner Radii
Characteristics
  Tightened curb radii at corner
  Can be achieved through curb, paint or attenuators
Typical use
  Intersections with few large turning vehicle types
Considerations
  Design vehicle
  Pedestrian crossing
  Cost
  Street operations
  Drainage
Horizontal Control

## Slide 18: Chicane
Characteristics
  Devices causing the deflection of vehicle travel direction – often multiple times within a segment
  On streets with parking on one side, can be made by shifting parking from one side to the other
Typical use
  Low volume residential streets
Considerations
  Can be accomplished with paint, planting, on-street parking and/or vertical elements
  Street maintenance and sweeping
  Cost
Horizontal Control

## Slide 19: Mini Roundabout
Characteristics
  Painted or curbed circle in the middle of an intersection to deflect vehicle line of travel
  Maintains existing curblines
  Truncates driver sightline
Typical use
  Intersection of low volume residential streets
  Few large vehicles
  Typically replaces 4-way stops
Considerations
  Community support for maintenance and sponsorship
  Cost
Horizontal Control

## Slide 20
4. Operational controls:
CHANGE HOW MOTORISTS MAY USE THE STREET
Signs and regulations

## Slide 21: Stop Controls
Characteristics
  Signage or signals
  Includes 2-way and 4-way stops, yields, and signalized controls
Typical use
  Intersections
Considerations
  Traffic volumes and direction of travel to meet warrants
  Sightlines
  Often low compliance for 4-way stop or yield controls
  Braking and acceleration impacts
Operational Control

## Slide 22: one-way Street Operations
Characteristics
  Street operates in one direction only
  When used for traffic calming, intended to reduce traffic volumes by limiting access
Typical use
  Various street types
Considerations
  Network operations
  Unintended effects on vehicle travel speed and volume
Operational Control

## Slide 23: Opposing one-way
Characteristics
  Street changes direction at a cross street prohibiting through traffic
Typical use
  Minor streets intersection with larger volume streets
Considerations
  Network operations
  Legibility of signage
  Local access
  Consequences on street travel speeds
Operational Control

## Slide 24: Turn and access Restrictions
Characteristics
  Signage indicating turn or access restrictions
  May be temporal or perpetual
Typical use
  Various street types
Considerations
  Generally low compliance
  Enforcement challenges
Operational Control

## Slide 25: Diverter
Characteristics
  Device to prohibit the through movement of traffic
  Can provide through movement for other modes
Typical use
  Intersection of low volume streets with higher volume thoughways
  Eliminate cut through traffic or reduce traffic volumes
  In conjunction with neighborhood bikeways
Considerations
  Traffic operations and access
Horizontal Control

## Slide 26
5. TRY things out
Interim treatments can be used on a trial basis

## Slide 27: INTERIM Refuge Island
Characteristics
  Can be installed temporarily on a trial basis
Horizontal Control
A high-visibility crosswalk and pedestrian refuge island, built using interim materials (Seattle, WA)
Trial pedestrian refuge islands built from flexposts (Frankstown Ave., Larimer)

## Slide 28: INTERIM BUMPOUT
Characteristics
  Can be installed temporarily on a trial basis
  Can be permanent where issues like drainage prohibit concrete construction
Horizontal Control
  Interim curb extensions using paint and flexposts (Seattle, WA)

## Slide 29
6. IMPROVE PEDESTRIAN AND BIKE NETWORK
Marked crosswalks don’t necessarily mean safer
Slower speeds improve safety and yielding for everyone on the street
Neighborways: slow speed, low volume streets create safe and comfortable corridors for walking, jogging, biking, playing, etc.

## Slide 30: MARKED Crosswalk
Characteristics
  Legal crosswalks exist at (almost) every intersection
  Markings can show the location of a crosswalk at select locations
Typical use
  Low to moderate volume streets
  2-3 lanes
Considerations
  Crossing must be at safe location
  Lighting
  False sense of security: does not guarantee motorists will yield
  Does not reduce speeds
  Pair with refuge island/signage
Visual/Operational Control
High-visibility crosswalks can improve yielding to pedestrians when speeds are slow enough.

## Slide 31: Pedestrian Refuge Island
Characteristics
  Concrete island in middle of the street
Typical use
  Streets where there are long gaps between signalized intersections
  Where yielding is poor
  On wide streets
Considerations
  At intersections, can make turns more difficult for trucks or buses
  Maintenance
Horizontal Control
A concrete pedestrian refuge island provides a
place to wait and slows traffic (New York City)

## Slide 32: Neighborways
Characteristics
  Uses a combination of traffic calming treatments to slow traffic speed and volumes.
  Prioritizes walking, biking, jogging, playing, etc.
  Creates comfortable streets people of all ages and abilities.
Typical use
  Residential streets.
  Usually parallel to main routes that are busier and less comfortable.
Considerations
  Integrate wayfinding to help people find and stay on the Neighborway corridor.
Traffic Calmed Corridors

## Slide 33
7. NEXT STEPS
The traffic calming process

## Slide 34: Central Lawrenceville neighborway
  PHASE 1: SUMMER 2019
WILLOW STREET
44th
HATFIELD STREET
N

## Slide 35: TELL US WHAT YOU THINK
Write on map or use post-it notes to mark trouble spots.
Report paving/pothole concerns directly to 311.
Trouble Spots in Lawrenceville